## Slide 1: Fully Memristive Spiking Neural Network with Forward-Forward Learning
By OOI HONG YAN (PETER)

## Slide 2: Problem Description
Artificial intelligence (AI) is now the forefront of modern computing
Modern AI relies on backpropagation and matrix operations for learning
For fast speeds AI runs on the GPU to take advantage of parallelism instead of CPU’s sequential nature
Source: Comptoir-Hardware
Source: GeeksforGeeks

## Slide 3: Problem Description
To run AI’s, datacentres use enough power to power an entire city
By 2026, the total energy used by data centers globally is projected to reach up to 1,050 TWh. The entire UK uses about 280–300 TWh. 3.5x more!
For edge devices, power usage is too high for powerful models to be run on small hardware.
Source: Devopedia
Source: OchoBits

## Slide 4: Problem Description
Our brain only uses about 20W
Biological Abstraction – Models use highly abstract version of neurons
Neurons are much more complicated, using temporal spikes to encode information
Von Neumann Bottleneck - GPUs need to fetch data from the VRAM, creating a memory wall
Global Backpropagation – Requires storing complex computational graphs and has no biological basis
Source: GeeksforGeeks
Source: Noba Project (CC BY-NC-SA)

## Slide 5: SNN
Closer to biological neurons, uses spikes instead of a singular value
Information is encoded in the timing of the spikes
Instead of using energy every cycle, energy is dependent on spike activity
Can run much more efficiently on neuromorphic hardware
Problem: Uses mathematical approximations to fake the smooth curves needed for learning
Source: Kaizou.org

## Slide 6: Memristor
Unlike other fundamental components, resistance is dependent upon its previous history; hence it has “memory”
Generates continuous analog voltage trajectories
Because of this it remain differentiable, solving the issue of approximations
Problem: Current memristor implementations use global backpropagation
Source: Wikimedia (CC BY-SA)

## Slide 7: Fully Memristive Spiking Neural Networks (MSNN)
Memristive Integrate and Fire (MIF)
Parameters voltage (V), memristive conductance (G1,G2), capacitance (C) and device resistance (Ron/Roff)
Backpropagation through time (BPTT)
Source: Own Work (Reproduced with permission from X. Shi et al. 2025)
Source: Own Work

## Slide 8: Forward Forward
Replaces global backpropagation with 2 forward passes
1 Positive pass and 1 Negative pass
Greedy layer wise learning
Goodness is calculated by the activity of the neurons
Each layer learns by maximising goodness on positive pass and minimising it on negative pass
Source: snnTorch Docs (CC BY 4.0)

## Slide 9: My Contributions
Build upon the code that implements memristors
Integrate the forward-forward algorithm into the MIF
Evaluate it with against other models

## Slide 10: MSNN Forward Forward
Layers can be saved and checkpointed
Source: Own Work
Source: Own Work

## Slide 11: MSNN Forward Forward
Alpha
Data (batch)
Pos Data
Neg Data
Single batch – Single layer
Labelling
x pixels
Last Layer
x pixels

## Slide 12: MSNN Forward Forward
Single batch – Single layer
Last Layer
x pixels
Save Layer

## Slide 13: MSNN Forward Forward
Loaded Layer1
Last Layer
Single batch – Multi layer
……………….
x pixels
Loaded Layer n
x pixels
x pixels

## Slide 14: MSNN Forward Forward
Alpha
Data (batch)
Pos Data
Neg Data
Single batch
Labelling
x pixels
All Layers
Single batch learn process

## Slide 15: MSNN Forward Forward
Single batch learn process
Number of epochs
Dataset
Single batch learn process
Single batch learn process
Until all samples learned

## Slide 16: MSNN Forward Forward
Inference
Layer1
……………
Last Layer
x pixels
Next Layer
x pixels
x pixels
Positive Goodness
Positive Goodness
Positive Goodness
Layer1
Positive goodness sum =
500
Correct Sample
Wrong Sample
Positive goodness sum =
497
+
+

## Slide 17: System
Local Development
Python 3.13 and the PyTorch2 (CUDA 13.0) ecosystem.
NVIDIA GTX 1650 Ti mobile GPU
AMD Ryzen 7 4800H iCPU
16GB of 3200 MT/s SODIMM RAM
Colab and Kaggle
Python 3.11
NVIDIA T4

## Slide 18: Tests
Training Loss
Plotting data from logs
Isolated neuron
Semi-implicit vs Explicit Euler
Source: Own Work

## Slide 19: Experiment
Tested with MNIST, KMNIST and FashionMNIST
Source: Own Work

## Slide 20: Results
Source: Own Work
Update: There is also the 40 epoch MNIST which got 98.21%!

## Slide 21: Future Work
More datasets, like the DVS dataset
NoProp
Hormonal modulation networks
“Sleeping”
Implementation and benchmarks on real memristors

## Slide 22: Thank you! Feel free to ask any questions